## Slide 1: Bitwise Operations
Based on materials developed by Professor Joshua Fox

## Slide 2: The basics of bits and bytes
A bit (or binary digit) is a basic unit of data in computing
A bit can have a value of 0, or 1
  Unlike a decimal digit, which has a value of 0-9
A byte is made of 8 bits (commonly, though other sizes exist)
Data types are made of multiple bytes
A char is 1 byte, or an 8-bit integer (everything is a number, either integral or floating-point value)
A short is 2 bytes, or a 16-bit integer
An int is a 4 byte variable, or a 32-bit integer

## Slide 3: Calculating decimal values
In a base 10, or decimal, numbering system, place values are based on powers of 10
Thousands Place (10^3) | Hundreds Place (10^2) | Tens Place (10^1) | Ones Place (10^0)
8 | 9 | 3 | 5
8 x 1000 | 9 x 100 | 3 x 10 | 5 x 1
8000 | 900 | 30 | 5
8000 + 900 + 30 + 5 = 8935
Decimal value: 8,935
The sum of the products of each place value and its corresponding digit is the final value

## Slide 4: Binary numbering
In a base 2, or binary, numbering system, place values are based on powers of 2
Eight place (2^3) | Four Place (2^2) | Two Place (2^1) | One Place (2^0)
1 | 0 | 1 | 1
1 x 8 | 0 x 4 | 1 x 2 | 1 x 1
8 | 0 | 2 | 1
8 + 0 + 2 + 1 = 11
Binary value: 1011
The sum of the products of each place value and its corresponding digit is the final value

## Slide 5: Place values compared
10,000,000 | 1,000,000 | 100,000 | 10,000 | 1,000 | 100 | 10 | 1
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
The rules for calculating this is the same for any number system:
The final value is the sum of the products of each place value and its corresponding digit
11111111 in decimal is… 11,111,111
11111111 in binary is… 255
Base 10
Base 2
10,000,000 + 1,000,000 + 100,000 + 10,000 + 1,000 + 100 + 10 + 1
128 + 64 + 32 + 16 + 8 + 4 + 2 + 1

## Slide 6: Modifying bits indirectly
Code ultimately turns into bit operations. For example:
int x = 5;
A compiler translates this to instructions:
Set the bits of a memory location to the binary equivalent of 5, or 0101 (plus 28 leading zeroes, as int is a 32-bit type)
Whether you’re aware of it or not, this is always happening
Most computational processing ultimately ends up as:
“set these bits to these values” “check if these bits are equal to this value” “if so, set these OTHER bits to this other value” “if not, set THESE other bits to THIS other value”
A little dull when you think of it this way!
Not nearly as interesting as “draw this 3D model to the screen” “open this file and read its contents”
“connect to this remote web server”

## Slide 7: Modifying bits directly
Though we typically work with bits on a “higher level” we may want to get a little more control
Or possibly some extra efficiency in terms of memory usage
To change or check bits directly, we must use operators that work at a “lower level” -- the bit level
These are called bitwise operators

## Slide 8: Bitwise operators
Operator | Name
¦ | OR
& | AND
^ | XOR
~ | Negation
<< | Left shift
>> | Right shift
Not to be confused with logical operators:
logical OR: ||
logical AND: &&

## Slide 9: OR |
Compares bits of two values
If EITHER of the two bits are 1, the final result is 1
Used to combine groups of bits together, or turn bits ON
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result (ValueOne | ValueTwo)
? ? ? ?

## Slide 10: OR |
At least one of these is “on”, so the final result is on, or 1
Compares bits of two values
If EITHER of the two bits are 1, the final result is 1
Used to combine groups of bits together, or turn bits ON
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 ? ? ?

## Slide 11: OR |
Neither of these bits are on, so the result is a 0, or “off” bit
Compares bits of two values
If EITHER of the two bits are 1, the final result is 1
Used to combine groups of bits together, or turn bits ON
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 0 ? ?

## Slide 12: OR |
At least one of these is on, so the final result is on
Compares bits of two values
If EITHER of the two bits are 1, the final result is 1
Used to combine groups of bits together, or turn bits ON
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 0 1 ?

## Slide 13: OR |
At least one of these is on, so the final result is on
Compares bits of two values
If EITHER of the two bits are 1, the final result is 1
Used to combine groups of bits together, or turn bits ON
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 0 1 1

## Slide 14: OR |
Compares bits of two values
If EITHER of the two bits are 1, the final result is 1
Used to combine groups of bits together, or turn bits ON
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result (11)
1 0 1 1
This process is combining BITS, not VALUES
3 + 10 != 11
3 |= 10 == 11
8+0+2+1

## Slide 15: AND &
If BOTH bits are 1, the final result is 1
Useful for checking if a particular bit is turned on
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result (ValueOne & ValueTwo)
? ? ? ?

## Slide 16: AND &
BOTH of these bits are not on, so the final bit is off
If BOTH bits are 1, the final result is 1
Useful for checking if a particular bit is turned on
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
0 ? ? ?

## Slide 17: AND &
BOTH of these bits are not on, so the final bit is off
If BOTH bits are 1, the final result is 1
Useful for checking if a particular bit is turned on
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
0 0 ? ?

## Slide 18: AND &
BOTH of these bits are turned on, so the result is 1
If BOTH bits are 1, the final result is 1
Useful for checking if a particular bit is turned on
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
0 0 1 ?

## Slide 19: AND &
Only one of these bits is on, so the resulting bit is 0
If BOTH bits are 1, the final result is 1
Useful for checking if a particular bit is turned on
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
0 0 1 0

## Slide 20: AND &
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result (2)
0 0 1 0
0+0+2+0
This can be used to check if a specific bit is turned on:
if (someValue & 2 == 2)
{
// 2 bit is on }
someValue could be anything, but using AND with 2 means we ignore all but one specific bit:
? ? 1 ?
someValue: 1111
(someValue & 2 == 2) == true
someValue: 0000
(someValue & 2 == 2) == false
someValue: 1101
(someValue & 2 == 2) == false
someValue: 1010
(someValue & 2 == 2) == true

## Slide 21: Exclusive Or, XOR ^
If EXACTLY ONE of the two bits are 1, the final result is 1
If both are 0, the result is 0
If both are 1, the result is 0
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result (ValueOne ^ ValueTwo)
? ? ? ?

## Slide 22: Exclusive Or, XOR ^
Only one of these two is on, so the final bit is on.
If EXACTLY ONE of the two bits are 1, the final result is 1
If both are 0, the result is 0
If both are 1, the result is 0
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 ? ? ?

## Slide 23: Exclusive Or, XOR ^
Is EXACTLY ONE of the two bits on? No? The final bit is 0.
If EXACTLY ONE of the two bits are 1, the final result is 1
If both are 0, the result is 0
If both are 1, the result is 0
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 0 ? ?

## Slide 24: Exclusive Or, XOR ^
Is EXACTLY ONE of the two bits on? No? The final bit is 0.
If EXACTLY ONE of the two bits are 1, the final result is 1
If both are 0, the result is 0
If both are 1, the result is 0
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 0 0 ?

## Slide 25: Exclusive Or, XOR ^
Only one of these bits is on, so the final result is 1.
If EXACTLY ONE of the two bits are 1, the final result is 1
If both are 0, the result is 0
If both are 1, the result is 0
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result
1 0 0 1

## Slide 26: Exclusive Or, XOR ^
0 0 1 1
1 0 1 0
ValueOne (3)
ValueTwo (10)
Final result (9)
1 0 0 1
8+0+0+1

## Slide 27: NEGATION ~
An unary operator—it only has one operand
Inverts all of the bits of a value – 0s become 1, and 1s become 0
Usage: newValue = ~someValue; int someNumber = ~45;
1 1 0 0
0 0 1 1
Value (12)
~Value (3)

## Slide 28: Bit-shifting: << and >>
These operators move (shift) every bit in a value left or right a number of times specified by the right-hand operand
int value = 1;
value = value << 2; // Move every bit 2 spaces to the left
value <<= 1; // Move every bit 1 space to the left
0 0 0 1 == 1
value (1)
value <<= 2
0 1 0 0 == 4
value <<= 1
1 0 0 0 == 8
Left-shifting is equivalent to multiplying by 2^N, where N is the right-hand operand
<< 3 (multiply by 2^3, or 8)
<< 6 (multiply by 2^6, or 64)

## Slide 29: Right-shifting: Divide by 2^N
The same concept as left-shift, in reverse!
int value = 200;
value = value >> 3; // Shift 3 spaces right (divide by 2^3, or 8)
value >>= 1; // Shift 1 space right (divide by 2)
1 1 0 0 1 0 0 0 == 200
value (200)
value >>= 3
0 0 0 1 1 0 0 1 == 25
value >>= 1
0 0 0 0 1 1 0 0 == 12
Mathematically 25/2 == 12.5, but the bits don’t lie! (Also, integers can’t store floating-point numbers)
“new” bits are set to 0, and bits will “fall off the edge” of a value (and “disappear”)

## Slide 30: Bit fields
A bit field is, generally, just a collection of bits that are stored together
Practically speaking, basic data types can be used for this purpose
unsigned char 1 byte, or 8 bits (a bit field with 8 values)
unsigned int 4 bytes, or 32 bits (a bit field with 32 values)
We often think of a variable as storing ONE value, but what if we think of it as storing multiple?

## Slide 31: Problem: You need 8 booleans to represent some information
1 bool variable = 1 byte
8 bool variable = 8 bytes
1 unsigned char (made of 8 bits) = 1 byte
One unsigned char can store up to 8 bool values, for 1/8 the memory!
Why not just use a bool as a bitfield?
You COULD, but compilers often treat boolean data types a bit differently, and they may not work with other operations

## Slide 32: Example – tracking a video game character’s inventory
A character can carry the following items:
Flashlight
Pistol
Crowbar
Shotgun
Laser
Machine gun
Chainsaw
Rocket launcher
// 8 true/false values
bool items[8];
How could we track what the character is holding?
// Also 8 true/false values
// (0/1 values, same thing... ish)
unsigned char bitItems;

## Slide 33: Picking up an item
Flashlight
Pistol
Crowbar
Shotgun
Laser
Machine gun
Chainsaw
Rocket launcher
bool items[8];
unsigned char bitItems = 0;
items[0] = true; // Flashlight
bitItems |= 1; // turn on the 1 bit
items[1] = true; // Pistol
bitItems |= 2; // turn on the 2 bit
items[2] = true; // Crowbar
bitItems |= 4; // turn on the 4 bit
items[6] = true; // Chainsaw
bitItems |= 64; // turn on the 6 bit
bitItems |= (1 << 6); // an alternative
Why the 4 bit? Because binary “places” increase by power of 2 values:
8 4 2 1
0 1 1 1
The bit for the second item has the equivalent value of 2^2
1 << 6 == 64

## Slide 34: Dropping an item
Flashlight
Pistol
Crowbar
Shotgun
Laser
Machine gun
Chainsaw
Rocket launcher
bool items[8];
items[0] = true;
items[2] = true;
// Holding crowbar and flashlight
unsigned char bitItems = 5;
// Drop the crowbar
items[2] = false;
// Turn off the 4 bit
bitItems &= ~4;
What sorcery is this?!

## Slide 35
If OR is the “turn on” bitwise operator, what’s the “turn off” operator?
There isn’t one, so we have to combine two of them
The negation operator ~ and the AND operator &
Get the negation of the bits you want to turn off
AND the result with your original value
Turning off bits requires more work

## Slide 36: Turning off bits requires more work
bitItems = 5
flashlight == 1 PLUS
crowbar == 4
0 1 0 1
1. Get the value of bit(s) you want to turn off
(just the 4 bit, in this case, so a value of 4)
2. Negate that value (flip 0s to 1s and 1s to 0s)
0 1 0 0
4 == 0 1 0 0
~4 == 1 0 1 1
3. AND with the original value (Bits that are “on” for BOTH values will be on in the final result)
~4 == 1 0 1 1
bitItems == 0 1 0 1
bitItems &= ~4 == 0 0 0 1

## Slide 37: Random inventory for a character
bool items[8];
for (int i = 0; i < 8; i++)
{
int roll = randomInt(0, 1);
if (roll == 1)
items[i] = true;
}
// Bitfield version
unsigned char bitItems = randomInt(0, 255);
So… how does this work?
Let’s say the number generated was 172

## Slide 38: Random inventory for a character
172 == 1 0 1 0 1 1 0 0
128
64
32
16
8
4
2
1
Flashlight
Pistol
Crowbar
Shotgun
Laser
Machine gun
Chainsaw
Rocket launcher
if (bitItems & 128 == 128)
// we have a rocket launcher
172 == 1 0 1 0 1 1 0 0
128 == 1 0 0 0 0 0 0 0
Only one bit is turned on from (172 & 128) – the 128 bit

## Slide 39: Bit fields and enumerations
An enumeration (enum) can help with identifying bits
Instead of bit 4, bit 32, bit 128…
enum Items { FlashLight = 1, Pistol = 2, Crowbar = 4, Shotgun = 8, Laser = 16, MachineGun = 32, Chainsaw = 64, RocketLauncher = 128};
This may make your code a bit more readable
No more wondering what was item 16? Was the Shotgun 8, or 4?
// Pick up a laser
bitItems |= Items::Laser;

## Slide 40: Recap
Bitwise operations let you manipulate values on the bit level
You may do this to store more values in a smaller space for memory efficiency
You may do this for ease-of-use as well (i.e. it can make some aspects of your code a bit easier to work with)
These can be used in applications like cryptology and security, which go a bit beyond the scope of the course
These operations are lower-level, or closer to “computer language” than most other parts of a programming language